Beam-beam interactions and their compensation in RHIC and LHC
Hyung Jin Kim
Fermilab
June 4, 2009

---
Outline
- Motivation
- Beam-Beam Simulation Code (BBSIMC)
- Beam-beam and beam-wire interactions at RHIC
- Beam-beam simulation for wire compensation at LHC
- Electron lens at RHIC
Phys. Rev. ST Accel. Beams 12, 031001 (2009)
PAC’09 WE6PFP031 and WE6PFP032

---
Beam-beam interactions
- One of major sources which cause emittance growth or beam loss.
- Head-on at IPs and long-range at parasitic crossings.
- Expected to deteriorate beam quality in LHC, because of large beam intensity (1.2E11) and many bunches (30 parasitic crossings per IP).
- Need ways to reduce the effects:
  - Electron lens for head-on beam-beam compensation
  - Current carrying wire for long-range beam-beam compensation

---
Beam-beam force

---
Current carrying wire for long-range collision
- For a large separation distance at parasitic crossings, the strength of long-range interaction is inversely proportional to the distance.
- Its effect on a test beam can be compensated by current carrying wires which create just the same field.
- The advantage of such an approach consists of the simplicity of the method and the possibility to deal with all multipole orders at once.
- Beam-beam kick of round beam
Wire kick

---
Low energy electron lens for head-on collision
- Low energy electron beam which is matched to a profile of high energy colliding beam acts as a defocusing or focusing lens which compensates effect of the colliding beam.
- Beam-beam kick of round beam
Elens kick of Gaussian electron beam

---
Motivation
- In LHC, both head-on and long-range interactions are an issue due to large beam intensity and many bunches.
- Wire compensation will be tested in RHIC as a proof of principle.
- RHIC is also interested in head-on compensation with an electron lens to mitigate emittance growth.
  - Wire compensator: installed in 2006.
  - Electron lens: will be installed by end of 2011.

---
Beam-Beam Simulation Code (BBSIMC)
- 6D weak-strong tacking code
- Linear transfer matrices btwn nonlinear elements + nonlinear kicks at the nonlinear elements (thin lens approximation: sextupoles, mulitpoles, etc.)
- Beam-beam force: (1) Gaussian beam profile and (2) Poisson solver with FFT.
- Multiple-slice model for finite bunch length effects
- Lorentz boost to handle crossing angle collisions
- Modules: wire and electron lens compensation, BTF, and diffusion
- Fully parallelized with MPI.

---
Multiple slice model for head-on
- The strong bunch is divided into slices in a longitudinal direction to consider the finite bunch length effect of the beam-beam interaction.
- In the simulations, we applied 11 slices in the main IPs where the beta function is comparable with the bunch length.
- Each slice in a beam interacts with particles in the other beam in turn at the collision points.

---
Beam-Beam Force
Bassetti-Erskine formula for elliptic Gaussian beam profile
, where n* is number of particle per bunch, r0 is classical radius of particle, γ is Lorentz factor, and w is complex error function.

---
Beam-Beam Force
- Poisson solver with FFT for arbitrary beam profile
- Green function solution of Poisson equation
Using convolution theorem and inverse Fourier transform, one can get

---
Beam-beam and beam-wire interactions at RHIC

---
RHIC (Relativistic Heavy Ion Collider)
RHIC is used as a test bed for a wire compensator.
Head-on collisions at IP6/8.
In this study, simulate only Blue beam.

---
RHIC Parameters
	unit	Gold beam	Deuteron beam
Energy	Gev/n	100	107
Bunch intensity	1E9	1	134
Emittance (95%)	mm-mrad	18	18
Beta* at IP6	m	1	0.9
Beta(x,y) at wire location	m	(1100,390)	(1200,400)
Beam-beam parameter	1E-3	1.3	1.5
Nominal tune		(0.220, 0.231)	(0.235, 0.225)
Chromaticity		+2	+2
- Gold beam: gold(Blue)+gold(Yellow)
- Deuteron Beam: deuteron(Blue)+gold(Yellow)

---
Wire compensator in RHIC
- Two wires are installed (one for each beam).
- Phase advance betwn DX magnet and wire location is 5.7 degree.
- To compensate a single long-range, the current strength (IL) is required by (IL) = Nb * q * c, (Nb=bunch intensity, q=charge, c=speed of light).
- (IL) = 3.8 A-m (for Gold beam), 6.5 A-m (for Deuteron beam).
- Maximum wire strength is 125 A-m (Max. current is 50A).
To see the effect of wire, max. current is applied in the experiment and simulation.

---
Tune: wire position scan (RHIC)
The full lines are the curves calculated using the following expression:
Measurements and simulations also agree.
Simulation
Measurement
Data sets are obtained at gold beam at store energy. (Abreu, Fisher)

---
Gold beam: tune footprint (RHIC)
- Initial amplitude particles of 0-4 sigma.
- Resonance line: blue(9th order), cyan(12th order).
- Wire makes the tune spread wider.
- Resonance line below 12th order does not span the footprint.
12th
9th
With Wire
No Wire

---
Gold beam: Freq. Diffusion map (RHIC)
- Freq. Diffusion: tune change btwn first and second 1024 turns
  - DQ = log[sqrt(dQx^2 + dQy^2)]
- Red color corresponds larger diffusion.
- Wire increases the detuning of betatron tune.
- Wire makes the particle motions more chaotic at amplitude beyond 3 sigma.
No Wire
Wire:
50A 7sigma

---
Deuteron beam: tune footprint (RHIC)
- Initial amplitude particles of 0-4 sigma.
- Resonance line: blue(9th order), cyan(12th order).
- Final tunes of the deuteron beam due to the wire is closer to the diagonal
- Deuteron beam is free from the 9th and 12th order resonances.
12th
9th
With Wire
No Wire

---
Deuteron beam: Freq. Diffusion map (RHIC)
- No wire: mostly stable motion and only a small region with appreciable diffusion (only 12th resonance spanning)
- Wire changes the diffusion map significantly.
- Regions with large diffusion are observed even at 1 sigma amplitude even though no resonances below 12th order are spanned by the beam distribution.
No Wire
Wire:
50A 7sigma

---
Dynamic aperture (RHIC)
Gold beam
- Dynamic aperture is defined as the largest radial amplitude of particles that survive up to a certain time interval (1E6 turns).
- Wire distorts the boundaries near the vertical plane since the wire is moved in the vertical plane.
- With the wire powered, the DA in the two cases is nearly the same.
- Relative change of DA in Deuteron is bigger than Gold.
Deuteron beam

---
DA: Tune scan (RHIC gold-gold injection)
- At all wire separations, the largest dynamic apertures are distributed along the diagonal line Qx-Qy=0.02.
- The zone along Qx-Qy=0.03 has the smallest dynamic apertures.
- This scan indicates that the nominal tune is close to optimal.
- A sharper drop in dynamic aperture is observed near the 5th order resonance.
8 sigma
6 sigma
4 sigma

---
DA: Tune scan (RHIC gold-gold storage)
- At all wire separations, the largest dynamic apertures are distributed nearly along the diagonal between Qx=0.21 and Qx=0.24.
- The zone along Qx=0.25 has the small dynamic apertures.
- Nominal tune is in the region of large DA.
8 sigma
7 sigma
6 sigma

---
DA: Tune scan (RHIC deuteron-gold storage)
8 sigma
- Reduction of the DA is dominant near 4th resonance.
- A notable variation is seen near a circular band, i.e., Qx^2+Qy^2=0.21^2, when the beam-wire separation is small.
- Nominal tune is in the region of large DA.
7 sigma
6 sigma

---
BTF (beam transfer function) in RHIC
No Wire
- <x>: beam response to a small external transverse excitation at a given frequency.
- Transverse coupling is observed: One peak is close to 0.230 which is the horizontal tune, and the other is 0.225 which is the vertical tune.
- The shift of a peak location of the amplitude increases as the wire separation decreases.
- Width of the amplitude response widens.
- The shift is equivalent to the tune shift of zero amplitude particles.
Wire

---
Particle diffusion (RHIC)
Gold beam
- Simulation:
- Measurement: obtained by fitting the time-dependent loss rate after moving a collimator into and out from the beam.
- Dependence of diffusion coefficients on the initial action is exponential at small amplitudes and power law-like at larger amplitudes.
- Relative increase of diffusion coefficients at below 3 sigma amplitude for the deuteron beam is higher than that for the gold beam.
- Enhanced diffusion at near 3 sigma amplitude for the deuteron beam leads to significant increase of particle loss under the simulation conditions.
Deuteron beam

---
Loss rate due to beam-wire interaction (2008)
Loss rate
Wire separation

---
Particle loss rate (RHIC)
Gold beam
Onset of beam losses is observed at 8 and 9 sigma for gold and deuteron beams.
Separation at which there is a sharp rise in the loss rates agree with measurement.
- At fixed separation, loss of deuteron beam is higher than gold beam.
- Freq. diffusion with the wire shows greater diffusion in the deuteron case.
- Action diffusion is also larger in the deuteron beam.
- Both frequency and action diffusions seem to be better correlated with loss rates than the traditional short term indicators like footprints and dynamic aperture.
Deuteron beam

---
Long-range compensation (May 27, 2009)
- 100Gev proton-proton beam
- Bunch intensity: 1.7E11 p/bunch
- Yellow: tune(0.695,0.692), chrom(-1.5,1.0), ε(49,19)
- Blue: tune(0.691,0.688), chrom(2.3,-1.4), ε(24,-)
- Single long-range interaction near DX magnet.
- Wire current: 5A
R. Calaga, W. Fischer, G. Robert-Demoliaze

---
Summary (beam-wire interaction in RHIC)
- Betatron tune change due to the wire is well tracked by the simulation.
- Wire causes a significant increase in tune spread and diffusion for both gold and deuteron beams.
- Stability boundary near the vertical axis is linearly proportional to the beam-wire separation.
- Tune scan of DA identifies the betatron tune where DA is maximized for both gold and deuteron beams.
- BTF simulation and measurement identify betatron tune and transverse coupling.
- Action diffusion for the deuteron beam is larger than for the gold beam.
- Threshold separation at which there is a sharp rise in the loss rates agree to better than 1 sigma.
- Tune and action diffusions are closely related to particle loss rate.

---
Beam-beam compensation with current carrying wire at LHC

---
MODEL: Wire compensation in LHC
Nominal LHC: 2808 bunches → 30 parasitic crossings per IP
- A wire on each side of IP (total 4)
- Wire strength: (IL) = 83A-m
- Wire location: 105 m for IP
- At wire location:
     (betax,betay)=(1783,1792)
wire	Wire separation (sigma)
	horizontal	vertical
IP1_left	0	-8.56
IP1_right	0	+9.56
IP5_left	-9.33	0
IP5_right	+8.33	0
Koutchouk and Dorda

---
MODEL: Wire compensation in LHC
- 7 Tev proton-proton beam
- 2 head-on (IP1 & 5), beta* = 0.55m
- Beam intensity: 1.15E11 per bunch
- Crossing angle: 285 micro-rad
- Working point: (0.31,0.32)
- Chromaticity: (+2,+2)
- Emittance: 22.5 mm-mrad

---
Footprint (LHC)
- beam-beam parameter is 0.004.
- long-range interaction affects higher amplitude particles.
- Long-range interaction increases the tune spread of the high amplitude particles.
- footprint can be compressed to nearly the same spread as with the long-range interactions excluded.
With Wire
No Wire

---
Wire position scan: DA / beam loss (LHC)
(IL)=83A-m
- wire-beam separation distance is one of major wire parameters.
- separation is relative to average beam separation.
- angle-averaged dynamic aperture for off-momentum particles with dp = 3 sigma.
- dynamic aperture decrease linearly as the separation decreases.
- minimum particle loss between 0.9 and 1.0 separations.
- Proposed separtion is close to optimal one.
(IL)=83A-m

---
Freq. diffusion vs. wire separation (LHC)
- Small amplitude particles are unaffected by the beam-beam compensation.
- Freq. diffusion is improved at a certain separation ( 0.9 and 1.0 separations).
- suppress the tune change at large amplitude beyond 4 sigma.
0.8*d
0.9*d
1.0*d
1.1*d

---
DA vs. current (LHC)
- Current is varied from 40 Am to 150 Am ( 0.5 - 2 times 82.8 Am).
- DA stays roughly constant up to 100 Am, and falls down to 4.5 sigma.
- Beam dynamics are less sensitive to wire current than wire-beam separation.
		DA
separation	0.8-1.2	4 - 7 sigma
current	0.5-2.0	4.5-5.5 sigma

---
Summary (wire compensation in LHC)
- The results show that the particle loss is minimized at the wire separation between 0.9 and 1.0 of the reference separation.
- The separation corresponds to the one where the tune change of large amplitude particles is reduced.
- The dynamic aperture results show that the beam dynamics are more sensitive to the wire-beam separation than the wire current.

---
Beam-beam compensation with electron lens at RHIC

---
MODEL: Electron lens simulation at RHIC
- 1.7E11 bunch intensity is achieved at Run-08.
- For > 2E11 intensity, large beam loss is expected (2/3, 7/10 resonance).
- Elens installation by end of 2011.
- 250 Gev p-p beam
- 2 head-on (IP6 & 8), beta* = 0.5m
- Beam intensity: 2E11 per bunch
- Working point: (0.695,0.685)
- 1 e-lens at IP10 , beta = 10m
- NL: sextupoles/IR multipoles
elens

---
Electron Lens Requirement
- For full tune-spread compression
  - Electron beam profile should match proton profile at IP ( Gaussian)
  - Electron beam intensity should be Ne = N_ip * Np ; N_ip =2, Np=2E11
  - Full tune-spread compression does not help to reduce particle loss (BBSIMC, LIFETRAC, SIXTRACK)
- For reduction of particle loss
  - Electron beam profile should match proton profile for tune compression, but other profiles may be more suitable for reducing particle loss.
  - Electron beam intensity may be different from N_ip * Np

---
Electron beam profiles
1 sigma Gaussian
- exp(-0.5(r/sigma)**2)
- match to proton beam size
2 sigma Gaussian
- exp(-0.5(r/2sigma)**2)
Smooth Edge Flattop(SEFT)
- 1/(1+(r/4sigma)**8)

---
Gaussian Electron Lens ( 1 sigma)
Dynamic Aperture
Footprint
1x bbc fully compensates footprint.
Footprint folding is observed.
DA is increased at 1/8x bbc
1x bbc = beam-beam compensation with Ne = Nip * Np = 2*2E11

---
Gaussian Electron Lens ( 1 sigma)
NO elens
- Freq. diffusion: tune change btwn first and second 1024 turns
  - DQ = log[sqrt(dQx^2 + dQy^2)]
- 1x bbc: decrease tune change at small amp. but increase at large amp.
- 1/8x bbc: decrease tune change at both small and large amp.
1/8x bbc
1x bbc

---
Gaussian Electron Lens (1 sigma)
Particle loss
1x BBC
NO BBC
1/8x BBC
- Small Ne reduces beam loss: Ne < 0.5 Nip * Np
  - (loss with 1x bbc)/(loss with NO bbc) ~ 600%
  - (loss with 1/8x bbc)/(loss with NO bbc) ~ 30%

---
Comparison of electron beam distributions
Profile	Intensity / (N_ip*Np)	Dynamic aperture / (sigma)	Particle loss / (Relative to NO elens)
1 sigma Gaussian	1/2	5.10	115%
	1/4	5.44	63%
	1/8	5.63	30%
2 sigma Gaussian	2	5.05	10%
	1	5.40	8%
	1/2	5.63	6%
SEFT	2	4.77	22%
	1	5.47	6%
	1/2	5.57	6%
Below threshold current with 2 sigma Gaussian and SEFT profiles, particle loss is relatively insensitive to electron lens current variations.

---
Summary (elens compensation in RHIC)
Full tune-spread compression causes footprint folding and increases particle loss. Partial tune-spread compression without inducing footprint folding may reduce particle loss.
Tune diffusion is closely related to particle loss.
There is a threshold electron beam intensity below which beam life time is increased
Particle losses for 2 sigma Gaussian and SEFT profiles are relatively insensitive to intensities below threshold.
Wider electron beam profile than proton at elens location is found to increase beam life time. Validation with better statistics in progress.
Profile	Threshold (N_ip*Np)
1 sigma G	0.5
2 sigma G	2
SEFT	4

---
Summary
Simulations of wire-beam interaction in RHIC agree well with experiments.
Measurements with wire compensation in RHIC are in progress.
Wire compensaton in LHC reduces beam loss and the proposed wire separation distance is close to optimal.
Electron lens is benefical to reduction of beam loss in RHIC. Wider electron lens profiles are better.

---
Thank you

---
Electromagnetic lens (current carrying wire)
For a finite length of a wire embedded in the middle of a drift and tilted in pitch and yaw angles, the transfer map of a wire is
, where T represents the tilt of the coordinate system by horizontal and vertical angles to orient the coordinate system parallel to the wire, D is the drift map with a length L/2, and M is the wire kick integrated over a drift length

---
Gaussian Electron Lens ( 2 sigma)
Dynamic Aperture
Footprint
DA is increased at 1/2x bbc
Peak of 4x bbc electron beam profile is matched to that of 1x bbc at 1 sigma Gaussian.

---
Gaussian Electron Lens ( 2 sigma)
NO elens
Tune Diffusion
- 4x bbc: decrease tune change at small amp. but increase at large amp.
- 1/2x bbc: decrease tune change at both small and large amp.
1/2x bbc
4x bbc

---
Gaussian Electron Lens ( 2 sigma)
Particle loss
NO BBC
4x BBC
1/2x BBC
1x BBC
2x BBC
- Small Ne reduces beam loss:
  - (loss with 1/2x bbc)/(loss with NO bbc) ~ 10%

---
SEFT Electron Lens ( 4 sigma)
Dynamic Aperture
Footprint
- Shape of footprint with compensation is almost the same as without compensation.
- Dynamic aperture is almost the same up to 2x bbc.

---
SEFT Electron Lens ( 4 sigma)
NO elens
Tune Diffusion
- 4x bbc: decrease tune change at small amp. but increase at large amp.
- 1/2x bbc: decrease tune change at both small and large amp.
1/2x bbc
4x bbc

---
SEFT Electron Lens ( 4 sigma)
Particle loss
NO BBC
2x BBC
4x BBC
1/2x BBC
1x BBC
- Small Ne reduces beam loss:
  - (loss of 1/2x bbc)/(loss of NO bbc) ~ 10%